## Slide 1: Biomedical Imaging Introduction
Sebastian Kozerke
Institute for Biomedical Engineering, University and ETH Zurich, Switzerland

## Slide 2
A picture is worth a thousand words

## Slide 3: Imaging across scales
Proteins : nm
1 : 109
Body : m
Synapse : msec
1 : 1010
Life : years

## Slide 4: Choosing Instruments

## Slide 5: Clinical Biomedical Imaging
X-Ray, Computed Tomography
Magnetic Resonance Imaging
Nuclear Imaging
Ultrasound Imaging

## Slide 6: Learning objectives
Explain physical and mathematical foundations
Characterize system performance using linear system theory
Define requirements and design basic diagnostic imaging system chain
Identify advantages and limitations of different imaging methods
Signal generation
Matter interaction
Signal detection
Image reconstruction
Transfer function
Depiction fidelity
Noise propagation
Performance metrics
Data acquisition
Data pre-processing
Data reconstruction
Data post-processing
Resolution power
Dose, Safety
Experimental use
Clinical use
1
2
3
4

## Slide 7: Agenda

## Slide 8: Agenda
-
Exercise #1
Exercise #2
Exercise #3
Exercise #4
Exercise #5
Exercise #6
Exercise #7
Exercise #8
Exercise #9
Exercise #10
Exercise #11
Exercise #12
-

## Slide 9: Exercises
Matlab based (in groups of two); problem solving
13-15 HG E7 Lecture
15-16 HG E7 Exercise (preparation)
Tue
Wed
Thu
Fri
Sat
Sun
Mon
Tue
Exercise #X
15-16 HG E7 Exercise (solution, discussion)
13-15 HG E19 Computer room
Mon <23:59 Submit Solution in Moodle

## Slide 10: Activity
?
My expertise in Matlab programming is ...
Basic
Intermediate
Excellent
What is Matlab?

## Slide 11: Exam
Type Written, closed-book Personal 2-page formulary
Duration 120 min
Grading Submitted exercise results are graded.
A maximum bonus of 0.25 can be achieved and is added to the exam grade if a minimum of 9 exercises has successfully been accomplished.

## Slide 12: Lecture notes
Handouts + Exercises
https://moodle-app2.let.ethz.ch/course/view.php?id=11546
Book
Introduction to Medical Imaging
Cambridge University Press
Nadine Barrie Smith, Andrew Webb
www.library.ethz.ch  online access

## Slide 13: Book
Chapter 2.2-2.3

## Slide 14: Electromagnetic radiation
Radiation absorption
Electric field:
Magnetic field:
Wave speed:
Energy:
Notes: G-rays: <10 pm
X-rays: 10 pm – 10 nm
UV: 10 nm – 400 nm
Light: 400 nm – 750 nm
IR: 750 nm – 500 um
MW: 500 um – 10 cm
RF: >10 cm

## Slide 15: Electromagnetic wave attenuation
Electric field E0
Wave attenuation
Electric field E
Position
Frequency dependent attenuation coefficient

## Slide 16: Attenuation
Wavelength [nm]
Notes: Red laser = 650 nm
Green laser = 530 nm

## Slide 17: Attenuation
https://www.osa-opn.org/home/articles/volume_26

## Slide 18: Biomedical Imaging
X-ray Imaging
Radiation absorption
Notes: G-rays: <10 pm
X-rays: 10 pm – 10 nm
UV: 10 nm – 400 nm
Light: 400 nm – 750 nm
IR: 750 nm – 500 um
MW: 500 um – 10 cm
RF: >10 cm

## Slide 19: Biomedical Imaging
Imaging Mode: X-ray Imaging
Probe: X-ray photons
Wavelength: 10 pm – 10 nm
Matter interaction: absorption, scatter
Modalities: Projection imaging Digital Subtraction Angiography (DSA) Computed tomography
Chapter 2.1-2.18

## Slide 20: Wilhelm Conrad Röntgen, 1845-1923
Notes: Notes
When the German physicist Wilhelm Conrad Röntgen did experiments on Cathode ray's with a Crookes tube, he discovered while working, that a plate of barium platinocyanide (fluorescent crystals) on a nearby table in his workroom glowed when he activated the tube. Even when he covered the tube with black material it kept glowing. Roentgen named this new phenomena X-Rays.
Wilhelm Conrad Röntgen (in English: "William Conrad Roentgen") (March 27, 1845 – February 10, 1923) was a German physicist, of the University of Würzburg, who, on November 8, 1895, produced and detected electromagnetic radiation in a wavelength range today known as x-rays or Röntgen Rays, an achievement that earned him the first Nobel Prize in Physics in 1901.
Röntgen was born in Lennep (now a part of Remscheid), Germany, to a clothmaker. His family moved to Apeldoorn in the Netherlands when he was three years old. He received his early education at the Institute of Martinus Herman van Doorn. He later attended Utrecht Technical School, from which he was expelled for producing a caricature of one of the teachers, a "crime" he claimed not to have committed.
In 1865, he tried to attend the University of Utrecht without having the necessary credentials required for a regular student. Hearing that he could enter the Federal Polytechnic Institute in Zurich, today the ETH Zurich, by passing its examinations, he began studies there as a student of mechanical engineering. In 1869, he graduated with a Ph.D. from the University of Zurich.
In the next experiments he used photographic material and made his first X-Ray picture, the hand of his wife Anna Bertha!

## Slide 21
Generation of X-rays
Probe
Matter interaction
Detection
Image production

## Slide 22: Generation
fast electrons
target with heavy atoms
X-ray photons
Electrons interact with inner e- shells of target (X-rays are not radioactive!)
Notes: Blackboard
-> radiation consists of quanta
-> radiation energy is integer multiple of single quantum energy
-> single quantum energy depends on frequency -> Planck: E = h   = e  U (h = 6.6210-34 Js; 1 Js = 1 W/s2)
-> because of energy quantization radiation can be considered a particle stream (particle = photon)
-> E = m  c2 -> impulse of photon: p = m  c = h   / c (photons always travel at speed of light)
Notes
The electronvolt (eV) is the amount of kinetic energy gained by a single unbound electron when it passes
through an electrostatic potential difference of one volt, in vacuum. In other words, it is equal to one volt
(1 volt = 1 joule per coulomb) times the charge of a single electron (in coulombs). 1 eV = 1.610−19 J

## Slide 23: Generation – X-ray tube
Acceleration of electron in vacuum tube ( UA = 30-200 kV, IA = 50-100 mA)
Notes: Blackboard
-> wanted: min = h  c / e  U (U = 100 kV)
-> min = 6.610-34 Js  3108 m/s / 1.610-19 C / 1105 V = 1.25  10-11 m = 12.5 pm (remember: 1V = 1J/C)
Notes
-> 1 ångström (Å) = 10–10 metres = 0.1 nm = 100 pm
->  of typical diagnostic X-rays: 10 pm-10 nm

## Slide 24: Generation – Bremsstrahlung
Fast-moving electron decelerates when it swings around a heavy nucleus:
  electron interacts with electrons in outer shells
  energy depends on distance at which electron passes nuclei
  spectrum continuous 0 -> Emax
  interaction depends on Z value and E of electrons
electron
nucleus
fast
slower
X-ray photon
c
Notes: Notes
Bremsstrahlung (help·info), (from the German bremsen, to brake and Strahlung, radiation, thus, "braking radiation" or "deceleration radiation"), is electromagnetic radiation produced by the acceleration of a charged particle, such as an electron, when deflected by another charged particle, such as an atomic nucleus. The term is also used to refer to the process of producing the radiation. Bremsstrahlung has a continuous spectrum. The phenomenon was discovered by Nikola Tesla during high frequency research he conducted between 1888 and 1897.

## Slide 25: Generation – Characteristic radiation
+
electron
K
L
+
K
L
photo electron
“hole”
+
K
L
Fast-moving electron interacts tightly with bound electrons in target:
  K-shell electron is ejected
  Electron energy Eelectron > Ebinding, K
  Discrete energy of emitted radiation E = Ebinding,K – Ebinding,L
1)
2)
3)
Notes: Blackboard
-> emitted photon energy: ΔE = EN-EK = h  
-> exercise: what is the maximum energy of X-rays from a tungsten target?
-> solution: maximum energy x-rays are generated if a zero-energy electron jumps onto K shell
-> binding energy of electrons Ebinding = 13.6 eV  Z2eff
-> Zw = 74 -> Emax = h   = 13.6 eV (74-2)2 = 70.5 keV (Zeff ~ (Z–2) for nuclei with large Z since electrons with l=0 shield nuclei)
-> min = h  c / Emax = 610-34 Js  3108 m/s / ( 70.5103/1.61019 J) = 40 pm

## Slide 26
Interaction of X-rays
Probe
Matter interaction
Detection
Image production

## Slide 27: Attenuation – Photo effect
+
+
photo electron
“hole”
+
1)
Photo effect leads to total absorption of photon:
  Generation of characteristic x-ray radiation with low energy
  Photo electrons cause biological “damage”  “ionizing radiation”
  Probability ~   Z3/E3
2)
3)
incident photon
Notes: Blackboard
-> energy of incident photon EIncidence = EEjection + ½  me  2

## Slide 28: Attenuation – Compton effect
Back-scatter
Side scatter
Forward scatter
incident photon
recoil electron
Compton effect leads to photon “bouncing”:
  Photon loses (part of) its energy to kinetic energy of electron
  Detection of photon changes
  Recoil electron responsible for “biological” damage
  Probability ~ /E
scattered photon
Notes: Blackboard
-> Compare with billiard hit -> sketch photon hitting an electron a) before hit b) after hit (after hit impulse of photon is p’, of electron P’e)
-> conservation of energy: p  c + mc2 = p’  c + E’e -> ( p – p’ + mc)2 = ( E’e/c )2
-> conservation of momentum: p – p’ = p’e
-> square both sides: p2 – 2pp’+p’2 = p’e2 (p  p’ = p  p’  cos )
-> further calc
-> ’- = h/(mc)  (1-cos ) (Compton effect)
-> Scatter problem!

## Slide 29
Detection of X-rays
Probe
Matter interaction
Detection
Image production

## Slide 30: Projection Imaging
Detector
Aluminum filter
Chemical reaction/ Light/Electrons
Probe
Matter interaction
Detection
Image production
Incident x-rays
Transmitted/ scattered X-rays
Notes: Notes
-> Low energy photons do not reach the detector
- absorbed in x-ray tube material and patient (Dose)
- No contribution to the image
-> Inherent filtering in tube (glass, oil, target)
-> Additional filtering to reduce patient dose (aluminum sheets between

## Slide 31: Projection imaging – Image intensifier
scintillating screen + photocathode
e-
e-
e-
e-
e-
UDC
photoanode + digital
output screen
incident radiation
Notes: Notes
An X-ray image intensifier (XRII) refers to a special image intensifier device used in medical imaging involving x rays. It consists of an input window, input phosphor, photocathode, vacuum and electron optics, output phosphor and output window. It allows for lower x-ray doses to be used on patients by magnifying the intensity produced in the output image, enabling the viewer to easily see the structure of the object being imaged.

## Slide 32: Projection Imaging – Contrast
bone
muscle
fat
Linear attenuation coefficient
energy
Notes: Blackboard
-> scetch object with bone and soft tissue
-> illustrate weighted average of  in case of heterogeneous composition along d

## Slide 33: Projection Imaging – Contrast
Large contrast between bone and tissue/air
Very little contrast among different tissues
Notes: Blackboard
-> I/I0=exp(-d) -> display  ~ -log(I/I0)
-> calculate maximum contrast between air and average biological tissue with d = 20 cm (and =0.35 cm-1 w/o bone or air): I/I0 = exp(-d) = exp(-7) = 1/1000
-> calculate maximum contrast between air and bone tissue with d = 20 cm (and =0.7 cm-1): I/I0 = exp(-d) = exp(-14) = 8/10000000

## Slide 34
Computed Tomography
Probe
Matter interaction
Detection
Image production

## Slide 35: Projection versus Tomographic imaging
Projection imaging
= 3D structures are collapsed onto 2D image:
- details are obscured - low soft-tissue contrast - not quantitative
Tomographic imaging
= 3D structure is resolved:
- slices (“gr: Tomos = slice”)
- Computed image reconstruction
- Projection imaging and CT share same principles of x-ray generation, interaction, detection

## Slide 36: CT – Reconstruction problem
Adapted from Kalender WA, Computed Tomography, ISBN 3-89578-216-5

## Slide 37: Godfrey Hounsfield, 1919 – 2004
Notes: Sir Godfrey Newbold Hounsfield CBE (28 August 1919 – 12 August 2004) was an English electrical engineer who shared the 1979 Nobel Prize for Physiology or Medicine with Allan McLeod Cormack for his part in developing the diagnostic technique of computerized axial tomography (CAT).His name is immortalised in the Hounsfield scale, a quantitative measure of radiodensity used in evaluating CAT scans. The scale is defined in Hounsfield units (symbol HF), running from air at -1000 HF, through water at 0 HF, and up to bone at +1000 HF.

## Slide 38: CT – Principle
Adapted from Kalender WA, Computed Tomography, ISBN 3-89578-216-5

## Slide 39: CT – Image reconstruction
Adapted from Kalender WA, Computed Tomography, ISBN 3-89578-216-5

## Slide 40: CT – Applications

## Slide 41: CT – Applications
Adapted from Kalender WA, Computed Tomography, ISBN 3-89578-216-5

## Slide 42: Biomedical Imaging
Nuclear Imaging
Radiation absorption
Notes: G-rays: <10 pm
X-rays: 10 pm – 10 nm
UV: 10 nm – 400 nm
Light: 400 nm – 750 nm
IR: 750 nm – 500 um
MW: 500 um – 10 cm
RF: >10 cm

## Slide 43: Biomedical Imaging
Imaging Mode: Nuclear Imaging (SPECT, PET)
Probe: -ray photon, positron -ray photons
Wavelength: 2 pm – 100 pm
Matter interaction: absorption, scatter, pair production
Modalities: SPECT (Single Photon Emission Tomography ) PET (Positron Emission Tomography)
Chapter 3.1-3.21

## Slide 44
Positron Emission
Probe
Matter interaction
Detection
Image production

## Slide 45: PET – Positron Emission
Isotope Half-life
Carbon-11 20 min
Nitrogen-13 10 min
Oxygen-15 2 min
Fluorine-18 110 min
Gallium-68 68 min
Rubidium-82 1.25 min
Positron
Fluorodeoxyglucose (FDG)

## Slide 46
Positron Annihilation
Probe
Matter interaction
Detection
Image production

## Slide 47: PET – Annihilation
Coincidence detection of two g-rays gives information on location of
positron-electron anihilation (not on location of radionuclide)
positron emitting radionuclide
e-
g(511 keV)
g(511 keV)
Compton scattering

## Slide 48
Coincidence Detection
Probe
Matter interaction
Detection
Image production

## Slide 49: PET – Detector
g - rays
Scintillation Detector
Coincidence Detection
Image courtesy of HUG

## Slide 50
Image Production
Probe
Matter interaction
Detection
Image production

## Slide 51: PET – Image Production
Raw data image
(Back Projection)
Slide courtesy of Markus Rudin, AIC
Regridding to
Cartesian frame
Filtered Image
(e.g. Hanning Filter)
Lines of Response (LoR’s)

## Slide 52: FDG – PET
www.wikipedia.com
Notes: Oncology: PET scanning with the tracer fluorine-18 (F-18) fluorodeoxyglucose (FDG), called FDG-PET, is widely used in clinical oncology. This tracer is a glucose analog that is taken up by glucose-using cells and phosphorylated by hexokinase (whose mitochondrial form is greatly elevated in rapidly-growing malignant tumours). A typical dose of FDG used in an oncological scan is 200-400 MBq for an adult human. Because the oxygen atom which is replaced by F-18 to generate FDG is required for the next step in glucose metabolism in all cells, no further reactions occur in FDG. Furthermore, most tissues (with the notable exception of liver and kidneys) cannot remove the phosphate added by hexokinase. This means that FDG is trapped in any cell which takes it up, until it decays, since phosphorylated sugars, due to their ionic charge, cannot exit from the cell. This results in intense radiolabeling of tissues with high glucose uptake, such as the brain, the liver, and most cancers. As a result, FDG-PET can be used for diagnosis, staging, and monitoring treatment of cancers, particularly in Hodgkin's disease, non Hodgkin's lymphoma, and lung cancer. Many other types of solid tumors will be found to be very highly labeled on a case-by-case basis-- a fact which becomes especially useful in searching for tumor metastasis, or for recurrence after a known highly-active primary tumor is removed. Because individual PET scans are more expensive than "conventional" imaging with computed tomography (CT) and magnetic resonance imaging (MRI), expansion of FDG-PET in cost-constrained health services will depend on proper health technology assessment; this problem is a difficult one because structural and functional imaging often cannot be directly compared, as they provide different information. Oncology scans using FDG make up over 90% of all PET scans in current practice.

## Slide 53: FDG – PET
www.wikipedia.com
Notes: Oncology: PET scanning with the tracer fluorine-18 (F-18) fluorodeoxyglucose (FDG), called FDG-PET, is widely used in clinical oncology. This tracer is a glucose analog that is taken up by glucose-using cells and phosphorylated by hexokinase (whose mitochondrial form is greatly elevated in rapidly-growing malignant tumours). A typical dose of FDG used in an oncological scan is 200-400 MBq for an adult human. Because the oxygen atom which is replaced by F-18 to generate FDG is required for the next step in glucose metabolism in all cells, no further reactions occur in FDG. Furthermore, most tissues (with the notable exception of liver and kidneys) cannot remove the phosphate added by hexokinase. This means that FDG is trapped in any cell which takes it up, until it decays, since phosphorylated sugars, due to their ionic charge, cannot exit from the cell. This results in intense radiolabeling of tissues with high glucose uptake, such as the brain, the liver, and most cancers. As a result, FDG-PET can be used for diagnosis, staging, and monitoring treatment of cancers, particularly in Hodgkin's disease, non Hodgkin's lymphoma, and lung cancer. Many other types of solid tumors will be found to be very highly labeled on a case-by-case basis-- a fact which becomes especially useful in searching for tumor metastasis, or for recurrence after a known highly-active primary tumor is removed. Because individual PET scans are more expensive than "conventional" imaging with computed tomography (CT) and magnetic resonance imaging (MRI), expansion of FDG-PET in cost-constrained health services will depend on proper health technology assessment; this problem is a difficult one because structural and functional imaging often cannot be directly compared, as they provide different information. Oncology scans using FDG make up over 90% of all PET scans in current practice.

## Slide 54: PET – CT
From Kalender WA, Computed Tomography, ISBN 3-89578-216-5
CT
PET
Fusion

## Slide 55: Biomedical Imaging
Magnetic Resonance Imaging
Radiation absorption
Notes: G-rays: <10 pm
X-rays: 10 pm – 10 nm
UV: 10 nm – 400 nm
Light: 400 nm – 750 nm
IR: 750 nm – 500 um
MW: 500 um – 10 cm
RF: >10 cm

## Slide 56: Biomedical Imaging
Imaging Mode: Magnetic Resonance (MR)
Probe: radiofrequency waves
Wavelength: 5 – 150 cm
Matter interaction: nuclear spin transitions
Modalities: Magnetic Resonance Imaging (MRI) Magnetic Resonance Spectroscopy (MRS) Functional MRI (fMRI)
Chapter 5.1-5.23

## Slide 57
Magnetic Resonance
Probe
Matter interaction
Detection
Image production

## Slide 58: Magnetic Resonance Imaging
Signal source2)
Radiofrequency transmitter
Position  Frequency
Radiofrequency antennae
Frequency  Position
Magnet1)
MRI system
1) 0.5-14 Tesla
2) 1H, 31P, 13C, 19F

## Slide 59: Signal source – Protons
Hydrogen
Oxygen
Proton has non-zero spin I=1/2
Oxygen has zero spin I=0
Hydrogen

## Slide 60: Signal source in external magnetic field
Magnetic field B0
Precession about B0 with Larmor frequency: 0= B0;  =42.6 MHz/T

## Slide 61: Signal source in external magnetic field
Magnetic field B0
Magnetization M
-
~
hB0
2kT
+
Population difference =
Excess of “up” spins at 1.5 Tesla: 5*10-6

## Slide 62: Magnetic Resonance Imaging
Signal source2)
Radiofrequency transmitter
Position  Frequency
Radiofrequency antennae
Frequency  Position
Magnet1)
MRI system
1) 0.5-14 Tesla
2) 1H, 31P, 13C, 19F

## Slide 63: Detection
Voltage U
Voltage U = /t~M
Magnetic field B0
Detector
Transmit radiofrequency (RF) energy

## Slide 64: Detectors

## Slide 65
MR Imaging
Probe
Matter interaction
Detection
Image production

## Slide 66: Magnetic Resonance Imaging
Signal source2)
Radiofrequency transmitter
Position  Frequency
Radiofrequency antennae
Frequency  Position
Magnet1)
MRI system
1) 0.5-14 Tesla
2) 1H, 31P, 13C, 19F

## Slide 67: Position  Frequency
B=B-B0
0
(z)= (B0+B)
“Lamor frequency”
z
Gz=dB/dz
Notes: Die Tonskala und die Frequenzskala lassen sich also ineinander umrechnen, allerdings ist der Zusammenhang nicht linear. Fortschreitende Oktavabstände (a1 - a2 - a3...) sind in der Tonskala äquidistant (man denke z.B. an die konstanten Oktavabstände auf der Klaviertastatur). Sie entsprechen jedoch nicht konstanten Frequenzintervallen, sondern die Frequenz verdoppelt sich jeweils von Oktave zu Oktave (a1 = 440 Hz, a2 = 880 Hz, a3 = 1760 Hz,...). Daraus ergibt sich folgender mathematischer Zusammenhang zwischen der Frequenz f0 eines Tones und der Frequenz fx eines um x Oktaven höheren Tones:
fx = f0 *2^x

## Slide 68: Fourier imaging
FT
Object space
Data space1)
Gy
Gz
Gx
RF
1) also: k-space; k = spatial frequency

## Slide 69: Data space  Object space
IFT
Object space
Data space1)
1) also: k-space; k = spatial frequency
IFT

## Slide 70: MRI – Anatomy

## Slide 71: MRI – Angiography

## Slide 72: MRI – Heart

## Slide 73
Ultrasound Imaging
Probe
Matter interaction
Detection
Image production

## Slide 74: Biomedical Imaging
Imaging Mode: Ultrasound
Probe: acoustic waves
Wavelength: 0.07 – 1.5 mm
Matter interaction: scattering, absorption
Modalities: Echography Doppler Imaging Thermal Therapy
Chapter 4.1-4.14

## Slide 75: Biomedical Imaging
Electromagnetic waves
Acoustic waves
Do NOT require medium to transmit
Energy stored in propagating electromagnetic fields
Wave velocity is constant
DO require medium to transmit
Energy transport by mechanical displacement
Wave velocity depends on medium properties
Notes: G-rays: <10 pm
X-rays: 10 pm – 10 nm
UV: 10 nm – 400 nm
Light: 400 nm – 750 nm
IR: 750 nm – 500 um
MW: 500 um – 10 cm
RF: >10 cm

## Slide 76: Ultrasound Imaging
Piezoelectric transducer
Acoustic wave
Scattering/absorption

## Slide 77: Ultrasound Imaging
High-resolution liver imaging
Color-Doppler flow imaging

## Slide 78: Ultrasound Imaging
3D Ultrasound – Aortic regurgitation
Philips Healthcare

## Slide 79: Activity
?
Arrange imaging methods according to wave frequency involved (high to low) …

## Slide 80: “The most important slides”
#1
#2
#3
#4
#5
#6
#7
#8
#9

## Slide 81: Contact information
Prof. Sebastian Kozerke
Phone: 044 632 3549
Email: kozerke@biomed.ee.ethz.ch
Prof. Klaas Pruessmann Phone: 044 632 6696
Email: pruessmann@biomed.ee.ethz.ch
Institute for Biomedical Engineering
Gloriastrasse 35 8092 Zurich